## Slide 1: Robotics hackathon
AJ DiDonato, Tim Lobl, Harika Lingareddy, Adam Udovich, Kate Brady

## Slide 2: Requirements
3 pi polulu
Example code to begin with
32 possible sensor combinations
Three choices
  Following the line, looking for the next intersection
  At an intersection, deciding what type of intersection it is.
  At an intersection, making a turn.
Follow a straight line and find the most optimal path in a maze without loops

## Slide 3: Goals
Have the robot go through the maze twice
  First time – it would figure out what the dead ends are and what the bad paths are
  Second time – it would find the most optimal path
Figure out how to store the path in memory

## Slide 4: challenges
Time
Learning curve
Handling work alongside robotics hackathon
Mac OS incompatibility
T-shaped junction

## Slide 5: Algorithm approach
Sensors return an integer
  Values less than 1000 indicate robot is to the right of the line
  Values greater than 3000 indicate robot is to the left of the line
When sensors are all white:
  U-turn necessary
  Erase previous steps in path to be replaced when we hit next junction

## Slide 6: Code Additions
Robot speed
  Change speed based on how off center the robot is from the line
  Slower wheel speeds to reduce overcorrection
Stopping criterion
  When sensors read all black

## Slide 7: Handling loops
Out of scope for this challenge
Need to track distance traveled to form a more complex map than just a string of turning decisions
  Keep tuples of relative location from start area where junctions occur and turn decision
  A*

## Slide 8: What we learned
The relationship between hardware and software
Working on a team

## Slide 9: Future improvements
If we had more time …
  Left hand rule or right hand rule
  8 possibilities
  Handling dead ends and intersections
  Replacement rules for finding the optimal path